## Slide 1: Laser Cutting My Maker Mark
My Maker Mark
Grade 6 | Term 1 | Week 10 (2 Nov to 6 Nov)
MY MAKER MARK
Technology and Career Centre, Dubai
Ms. Lubna Kakkengal and Mr. Dilan Devendra
Notes: Grade 6 TCD class, My Maker Mark Session 2 of 3 (2 hours). Students prepare their maker mark as a laser file with separate cut and engrave layers, design the outline of a keychain or name plaque, and watch their piece being laser cut by the teacher.

## Slide 2: Hook
How can a beam of light cut through wood?
A focused beam
A laser focuses light into a tiny, very hot point.
Cut
Full power and slow speed: it burns all the way through.
Engrave
Less power and fast speed: it only marks the surface.
In the UAE
Laser-cut patterns shade buildings across the country.
Notes: Play the hook video on the TCD website (lesson page, Hook Video tab). Then ask: How can a beam of light cut through wood? Video scenes: A focused beam: A laser focuses light into a tiny, very hot point. | Cut: Full power and slow speed: it burns all the way through. | Engrave: Less power and fast speed: it only marks the surface. | In the UAE: Laser-cut patterns shade buildings across the country. | Today: Turn your maker mark into a real keychain or plaque.

## Slide 3: Today's Learning
We are learning to (WALT)
We are learning to prepare a 2D design for the laser cutter and to understand how the laser cuts and engraves.
What I am looking for (WILF)
I can explain the difference between cutting and engraving.
I can set up a file with a cut outline and an engrave area.
I can choose a suitable size and material for my piece.
I can follow the laser cutter safety rules.
Notes: Read the learning goal together. Students rate themselves now (1 to 3 fingers) for each success criterion and again at the end.

## Slide 4: Warm-up: Cut or Engrave?
5 minutes
1
Pass around three sample pieces: one cut out, one engraved, one with both.
2
Students decide for each: was it cut, engraved or both? How can they tell?
3
Agree: cutting goes all the way through; engraving only marks the surface.
Notes: Warm-up (5 min): Pass around three sample pieces: one cut out, one engraved, one with both. Students decide for each: was it cut, engraved or both? How can they tell? Agree: cutting goes all the way through; engraving only marks the surface.

## Slide 5: Key Words
laser cutter
vector
raster
cut
engrave
kerf
plywood
acrylic
power
speed
Say each word with your partner. Which words do you already know?
Notes: Pre-teach vocabulary: laser cutter, vector, raster, cut, engrave, kerf, plywood, acrylic, power, speed. Point to the word wall.

## Slide 6: How the laser works
A laser focuses light into a tiny, very hot point.
It moves in lines across the material like a printer.
Vector lines are followed to cut or score.
Raster areas are filled line by line to engrave.
Notes: How the laser works: A laser focuses light into a tiny, very hot point. It moves in lines across the material like a printer. Vector lines are followed to cut or score. Raster areas are filled line by line to engrave. A laser cutter focuses light into a tiny, very hot point. It follows vector lines to cut through material and fills raster areas line by line to engrave the surface.

## Slide 7: Cut and engrave layers
Cut: a thin outline, usually set as a red hairline.
Engrave: filled black areas.
The outline goes around your whole piece.
Your maker mark sits inside as the engrave layer.
Think
Explain one of these points to your partner in your own words.
Notes: Cut and engrave layers: Cut: a thin outline, usually set as a red hairline. Engrave: filled black areas. The outline goes around your whole piece. Your maker mark sits inside as the engrave layer. In our files, a thin red hairline means cut, and a black filled area means engrave.

## Slide 8: Size, material and kerf
Keychain: about 50 mm, plaque: up to 80 by 50 mm.
We use 3 mm plywood or acrylic.
The laser burns away a little material, called the kerf (about 0.2 mm).
Add a 4 mm hole at least 3 mm from the edge for a keyring.
Notes: Size, material and kerf: Keychain: about 50 mm, plaque: up to 80 by 50 mm. We use 3 mm plywood or acrylic. The laser burns away a little material, called the kerf (about 0.2 mm). Add a 4 mm hole at least 3 mm from the edge for a keyring. The laser burns away a tiny amount of material called the kerf. Designers plan for it when parts must fit together.

## Slide 9: Laser safety
Only the teacher operates the laser.
Never leave the laser running unattended.
The lid stays closed and the extraction stays on.
Never look into the beam. Keep a fire blanket and extinguisher nearby.
Think
Explain one of these points to your partner in your own words.
Notes: Laser safety: Only the teacher operates the laser. Never leave the laser running unattended. The lid stays closed and the extraction stays on. Never look into the beam. Keep a fire blanket and extinguisher nearby. The laser burns away a tiny amount of material called the kerf. Designers plan for it when parts must fit together.

## Slide 10: From design to laser
1
Import your maker mark
2
Draw the outline shape
3
Add the keyring hole
4
Set cut and engrave layers
5
Teacher checks the file
6
Teacher runs the laser while you observe
Notes: Model each step. 1. Import your maker mark 2. Draw the outline shape 3. Add the keyring hole 4. Set cut and engrave layers 5. Teacher checks the file 6. Teacher runs the laser while you observe

## Slide 11: Safety First
Every time. No exceptions.
Only the teacher operates the laser cutter.
Stand behind the safety line while it runs.
Never open the lid during a job.
Extraction must be on before starting.
Report any smell of burning or smoke immediately.
Notes: Read each rule aloud. Students repeat the rule and show the action. Do not continue until every student can say the rules. Only the teacher operates the laser cutter. Stand behind the safety line while it runs. Never open the lid during a job. Extraction must be on before starting. Report any smell of burning or smoke immediately.

## Slide 12: Your task today
Import your maker mark into the laser software.
Draw a keychain or plaque outline and add a keyring hole.
Set the cut and engrave layers and check sizes.
Get the teacher's file check.
Observe your piece being cut and record the settings.
Worksheet
Laser File Planner
Notes: Independent practice. Import your maker mark into the laser software. Draw a keychain or plaque outline and add a keyring hole. Set the cut and engrave layers and check sizes. Get the teacher's file check. Observe your piece being cut and record the settings.

## Slide 13: Choose Your Challenge
Beginning
Use the ready-made circle keychain outline and place your maker mark inside.
On
Design your own outline shape with a hole and correct layers.
Above
Design a plaque with your maker mark and a short engraved motto, and calculate how many pieces fit on one sheet.
Notes: Students choose a level. Encourage them to try the next level once they finish.

## Slide 14: Live Quiz Time
1. Open the TCD website and tap Join a Quiz.
2. Enter the quiz code on the board.
3. Type your Student ID, first name and last name.
4. Answer 8 questions. Fast and correct answers score more points!
Quiz code: _ _ _ _ _ _
Notes: Instructor: open this lesson on the TCD website, press Start Live Quiz, and write the code on the board. Questions: 1. What does engraving do? 2. What does cutting do? 3. In our files, a thin red hairline means ... 4. What is kerf? 5. Who operates the laser cutter in TCD? 6. Why must the extraction be on? 7. A keyring hole should be at least how far from the edge? 8. Laser-cut patterns on UAE buildings are inspired by ...

## Slide 15: Reflect: Exit Ticket
What is the difference between cutting and engraving?
Which safety rule is the most important around the laser, and why?
Check your success criteria
I can explain the difference between cutting and engraving.
I can set up a file with a cut outline and an engrave area.
I can choose a suitable size and material for my piece.
I can follow the laser cutter safety rules.
Notes: Closure: Students compare finished pieces with their file. What changed? Exit ticket (slide 15). Pieces are kept for finishing next week.